## Slide 1: COURSE NAME:COMPUTER ARCHITECTURE AND ORGANIZATION COIURSE CODE: CS 220
LECTURER: L SHUMBA
CA : AVERAGE OF TWO TESTS
CONSULTATIONS: Tuesdays and Fridays

## Slide 2: LITERATURE

## Slide 3: Lecture 1/2:Distinction between computer architecture and computer organization
Computer Arch deals with those attributes of the computer that are visible to the programmer.
Details such as: Physical memory – Allocated and Available memory space
Instruction Set Architecture of the processor.

## Slide 4: Computer Architecture
The number of bits used to represent data types like integer , character , double
Input Output mechanism – Depends on programming language.
Technique for addressing memories – Depends on programming language

## Slide 5: Computer organization
It deals with how different components of a computer are linked together to meet the requirements specified by computer architecture Some organizational attributes are:
Hardware details – Such as RAM, Hard drive , graphic card technology used.

## Slide 6: Computer Organization
Peripherals Devices – How devices such as mouse and keyboard, connected to the computer.
Control signals. Generated from the above mentioned controls.
Note that all above mentioned aspects ( hardware technology, Peripheral connectivity and their signals ) are therefore invisible to the programmer.

## Slide 7: Example
Assume you are programmer and you are writing a program. Also suppose your program has the following features: 1- Loads data from memory 2- Stores that data in integer variables 3- Performs some calculations and then outputs that data on computer screen.

## Slide 8: Programming example
To write such a program, programmers are only concerned with the details visible to them – Computer Architecture. Therefore programmers do not care about the conversion of keywords input to useful computer instructions. Nor do we care about the underlying RAM technology used. For this reason we say that organization of components is invisible to the programmer.

## Slide 10: Components’ and Functions of a computer
Central Processing Unit (CPU)
Made up of:
Control Unit
Arithmetic and Logic units

## Slide 11: MAIN MEMORY
Made up of:
ROM (Read Only Memory)
RAM (Random Access Memory)
Secondary Storage

## Slide 12: INPUT/OUTPUT UNITS
Assignment: Computer Components function(s)/purpose(s)

## Slide 13: Strategies for different computer architectures
Many computer architectures
Ways of categorizing them:
(i)By Number of instructions executed per clock cycle
Many Computer Machines read and execute one instruction at a time

## Slide 14: Von Neumann machines
These include:
Complex Instruction Set Computer (CISC)
Reduced Instruction Set Computer(RISC)
Minimal instruction set computer (MISC)
Transport Triggered Architecture(TTA)
Digital Signal Processor(DSP)

## Slide 15: Von Neumann Machines
These also include:
Accumulator machines
Register machines
Stack machines

## Slide 16: Executing several instructions per clock
Other computers read and execute several instructions at a time(clock cycle)
Very long instruction word(VLIW), Super- Scalar execute a minimum of two instructions per clock cycle
Still hit the Von Neumann bottle-neck at some large number of instructions per clock

## Slide 17: Program memory
Program counter always refer to “program memory no matter what address is loaded into it
Normal reads and writes always go to “ data memory”

## Slide 18: Categorization based on connections between CPU and Main Memory
These are Princeton Machines
They use unified memory where a single address corresponds to a single place in memory
One can use that address to read and write data, or can load that address in a program counter to execute a code

## Slide 19: Categorization according to memory spaces
Harvard Machines
Program memory
Data memory

## Slide 20: HARVARD ARCHITECTURE

## Slide 21: Harvard architecture instruction and data flow

## Slide 22: Von Neumann architecture